## Slide 1
KEMET Noise Suppression Sheet FLEX SUPPRESSOR ® is effectively designed for high frequency noise that is generated from electronic devices. The flexible sheet is a polymer base, blended with micron-sized magnetic powders dispersed throughout the material. These sheets are effective for electromagnetic wave and resonance suppression and can be cut into a variety of shapes and sizes.
Features
RoHS compliant
1 MΩ/sq. typical surface resistivity
UL file N° E176124
Permeability range from 25 to 250
Operating temperature from –40°C to 105°C (FF1 & EFF4 125°C)
Operating frequency from 1 MHz to 40 GHz
Attenuation Characteristics
Part Number System
Refer to KEMET datasheets for full details
© KEMET Corporation. All Rights Reserved.
Series
EFF4
View FLEX SUPPRESSOR® here
(01)-
240X240
T0800
Thickness Code
01 = 0.1 mm
03 = 0.3 mm
10 = 1.0 mm
25 = 0.025 mm
50 = 0.05 mm
100 = 0.1 mm
Size Code 240X240 = 240 mm X 240 mm sheet
240X80 = 240 mm X 80 mm sheet
240X10M = 240 mm X 10 M roll
5X50M = 5 mm X 50 M tape
Adhesive Thickness Code Blank = No adhesive
T0800 = 0.003 mm
T2900 = 0.01 mm
Chart: Attenuation (dB) with Thickness t = 0.1 mm
| EFS | FS | EFG2 | EFG3 | FG1 | EFA | EFF4 | EFW | EFX6 | FF1 | FX5 | FW5
 | 4.6 | 4.4 | 2.5 | 3.3 | 2 | 2.6 | 4 | 6 | 4.5 | 3.6 | 4 | 6
@ 700 MHz
(1 MHz-3 GHz)
@ 2.4 GHz
(1 GHz-10 GHz)
@10 GHz
(3 GHz-40 GHz)
Consumer electronics
Telecommunications devices
Automotive infotainment
Suitable for noise-sensitive applications including:
LTE / Wi-Fi
LTE / Wi-Fi / 5G
FM / DVB / GPS / Wi-Fi
Applications
FLEX SUPPRESSOR®
NOISE SUPPRESSION SHEET, ROLL OR TAPE
Overview
Electrical Characteristics